## Slide 1
Ethan Wells
Week 9 progress
Goals for the week
Test printed sign cards using BuggyBot’s CM5 camera.
Progress for the week
Photographed 10 sign classes under three lighting conditions.
Prepared 329 camera crops with an OpenCV template-matching script.
Compared LISA, Mapillary, and combined models on the same crops.
Combined model: 329/329 correct (100% top-1).
Repository cleanup
Reorganized the Hardware and Model Training folders.
Updated maintained documentation and repaired moved-file links.
Hours spent on progress
7 hours
Notes: Hours: 7, provided by Ethan. Camera evaluation: Model Training/reports/sign_photo_test_results.md. Cleanup: commits fb6e532, f7cf81d, 0b7dd6f, b13ee66. Next-week goals are on slide 4.

## Slide 2
The combined model classified all camera crops correctly
Top-1 accuracy on the same 329 BuggyBot camera crops
LISA
47.7%
157 / 329
Mapillary
79.9%
263 / 329
Combined
100%
329 / 329
Sample camera crops: School sign
No light
Sunlight
Sunlight + artificial
Notes: Source: Model Training/reports/sign_photo_test_results.md. Three crops show the same class under each recorded condition; not three independent camera angles. Images: Sign Cards/Test Images/cropped/school/{no_light,sunlight,sunlight_and_artificial}/school_000.png.

## Slide 3
Camera accuracy by sign
Top-1 accuracy on the printed-card camera crops
Sign | Photos | LISA | Mapillary | Combined
Added Lane | 33 | 33.3% | 100.0% | 100.0%
Keep Right | 33 | 72.7% | 100.0% | 100.0%
Merge | 33 | 0.0% | 100.0% | 100.0%
Pedestrian Crossing | 33 | 100.0% | 100.0% | 100.0%
School | 33 | 0.0% | 100.0% | 100.0%
Signal Ahead | 33 | 51.5% | 100.0% | 100.0%
Speed Limit 25 | 33 | 100.0% | 100.0% | 100.0%
Speed Limit 45 | 33 | 21.2% | 0.0% | 100.0%
Speed Limit 65 | 33 | 0.0% | 0.0% | 100.0%
Stop | 32 | 100.0% | 100.0% | 100.0%
Mapillary: speed-limit failures
Every Speed 45 and Speed 65 crop was misclassified (0/33 each).
LISA: color mismatch is a factor
Training includes many grayscale / near-grayscale crops; all 329 camera crops are color.
Grayscale conversion raised LISA from 47.7% to 59.6% on these same photos. It does not explain every error.
Speed limits 30 and 35 were not photographed; they are not planned for the track.
Notes: Sources: Model Training/reports/sign_photo_test_results.md and sign_photo_test_report.json. Table values copied from by_class; 33 crops per class except Stop (32). Investigation on 2026-10-17: saved lisa_model.keras, no retraining. Same 329 crops, same 32x32 tf.image.resize preprocessing; grayscale = tf.image.grayscale_to_rgb(tf.image.rgb_to_grayscale(x)) on 0-255 floats. Original: 157/329 =47.7%; grayscale:196/329 =59.6%; 61 original errors fixed, 22 original correct predictions lost. This supports a sensitivity to color/preprocessing, not a causal attribution to training grayscale prevalence alone. Training crop contact-sheet inspection confirms many grayscale-looking images with small residual channel differences; avoid asserting the earlier 40% figure without a documented threshold. None of the 329 original camera crops had maximum pixelwise RGB channel spread <=2. Private reproducibility script: .codex-slide-work/build/paired_gray.py; outputs paired_grayscale_results.json and grayscale_analysis.json.

## Slide 4
Test limits and goals for next week
The classifier passed this crop test; the live pipeline remains to be tested
Test limits
329 photos represent about 30 setups; repeated frames are near-duplicates.
Cropping used each sign’s known class and matching artwork.
Distances and angles were not systematically varied in the recorded test.
Results measure cropped-sign classification; live sign detection and CM5 inference remain unverified.
Goals for next week
1. Connect the combined classifier to the CM5 camera and LCD pipeline.
2. Evaluate automatic sign crops without using the known class.
3. Capture new setups at measured distances and angles; track accuracy and inference time.
Notes: Sources: Sign Cards/README.md; README.md, current pipeline status. Next steps are proposed goals accepted by Ethan for the slides, not completed implementation. Conditions cover 10 classes x3 lighting settings (~30 setups). No evidence of a systematic distance/angle study in the manifest.